## Slide 1
Pedestrians and Cyclists at the Intersection: When and Where?
DS3 Applications, Topic 4, intersection K305
Week 1: literature review and first look at the data
Notes: Week 1 report. We read 5 related studies, compared them, and did a first count of the K305 data.

## Slide 2
Goal: find when and where VRUs use K305
Vulnerable road users (VRUs): pedestrians, cyclists and similar. We analyze their trajectories to find peak times, crossing areas and overlap with motor traffic.
288
files, 5 min each
24 h
one full day, 2026-10-14
10 Hz
about 10 frames per second
3.9 GB
JSON object lists
Each detection has: track_id, class_name, x/y/z position, size, yaw, velocity.
Planned outputs: 15-min counts, density heatmaps, typical routes, VRU-vehicle overlap zones.
Notes: Topic sheet: temporal profiles, trajectory-density maps, overlap of VRU and vehicle flows.

## Slide 3
K305: 2.3M pedestrian and 380k cyclist detections
Chart: Detections per class, full day (log scale)
| Car | Pedestrian | Van | Cyclist | Truck | Bus | Motorcycle
Detections | 7923960 | 2319595 | 487517 | 379603 | 284957 | 58699 | 39155
1
Pedestrians 20.2%, cyclists 3.3% of detections
Orange bars are the VRU classes we analyze.
2
No Scooter class in the labels
Scooters may be hidden in Cyclist or Motorcycle. To check.
3
Motorcycle is a question
Does the professor count powered two-wheelers as VRUs?
Source: our count over all 288 files (detections = one object in one frame).
Notes: Counts are detections, not unique people. Track IDs seem to restart per file and trucks look fragmented, so unique tracks need a separate check.

## Slide 4
None of 5 studies covers both groups for a full day
Study | Year | Sensor | Data | VRU classes | What we reuse
Saldivar-Carranza et al. | 2024 | Roadside LiDAR | 1 intersection (Utah), 24 h, 170k pedestrian points | Pedestrians only | 15-min bins, movement rules, wait times
Chen et al. (FLUID) | 2025 | Drone video | 3 intersections (China), 5 h, 20k+ road users | Pedestrians, mopeds | Grid heatmaps, TTC/DGT overlap filter
Utah crossing study* | 2025 | Video | 39 intersections, 5,589 crossings | Pedestrians only | Where and when people cross
Steinmaßl et al. (SIT-PET) | 2026 | Roadside LiDAR | 1 intersection (Salzburg), 2 years | Pedestrians, two-wheelers | Geofences, PET, ID fragmentation notes
Anowar (R-LiViT) | 2026 | LiDAR + RGB + thermal | 3 intersections (Germany), short sequences | Persons, bicycles, motorcycles, e-scooters | Day vs night, VRU-vehicle proximity
Our data: K305 | 2026 | Roadside object list | 1 intersection, 24 h, 10 Hz | Pedestrian, Cyclist (+Motorcycle) | Both groups, time and space
*Utah crossing study: abstract only, authors still to confirm. First four papers read in full.
Notes: Gap: no study separates pedestrians and cyclists over a full day in both time and space at one intersection.

## Slide 5
Prior work: VRUs are half of road users, fewer at night
Chart: VRU detections by class (R-LiViT)
| Person | Bicycle | Motorcycle | E-scooter
Detections | 21026 | 4142 | 456 | 389
Chart: Average objects per frame, day vs night
| Pedestrians | Vehicles
Day | 10 | 13.4
Night | 6.2 | 7.4
VRUs are 49% of all detections. Pedestrian density drops 38% at night, but VRU-vehicle pairs sit closer.
Source: Anowar (2026), R-LiViT dataset, 3 German intersections, image-plane analysis, no trajectories.
Notes: These numbers are from the paper, not from K305. Pixel distances, not real-world meters.

## Slide 6
Our gap: both groups, time and space, one full day
1
What studies do
Mostly vehicles, pedestrians only, or short recordings. Cyclists rarely analyzed on their own.
2
The gap
None of the studies we found compares pedestrians and cyclists over a full day, in time and space, at one roadside-sensor intersection.
3
What we do with K305
15-min count profiles, density heatmaps per class, typical routes, and VRU-vehicle overlap zones.
Risks from the papers: tracks split into several IDs, class labels that flip, and only one day of data.
Notes: ID fragmentation and class flipping are documented in SIT-PET and visible in our first count.

## Slide 7
Next: 10-week plan and open questions
Wk 1
Literature, roles
Wk 2-3
Parse data, clean, define zones
Wk 4-6
Counts, heatmaps, peak hours, midterm
Wk 7-8
VRU-vehicle overlap, validation
Wk 9-10
Figures, report, slides
Questions for the professor
Which classes count as VRUs: only Pedestrian and Cyclist, or also Motorcycle and scooters?
Is there a K305 layout or crossing map? Is more than one day of data available?
What is the final deliverable and deadline: report, slides, dashboard?
Notes: Week 1 goal is the literature review. Parsing the data into one table is the first task of week 2.